## Slide 1: Wood processes
Mr. Maiseroulle

## Slide 2: Primary processing
Harvesting Wood
  Felling
  Bucking
Sawmill Operations
  Bandsaw
  Circular Saw
  Portable Saw
Drying
Pulp and Paper Manufacturing

## Slide 3: Secondary processing
Forming Wood
  Bonding: Using heat and pressure to compact particles
    hardboard, particle board, OSB, plywood, panels
  Bending
    Wet Bending
    Dry Bending

## Slide 4: Secondary Processing
Milling: Removing material with cutting edges equally spaced either on a flat surface or round cylinder.
  Hand tools: Rasp, file
  Machines: Planer, router, jointer, shaper

## Slide 5: secondary Processing
Abrading: removing material by wearing away with random or multipoint cutting edges.
  Hand tools: Sanding block and sand paper
  Machine tools: Belt sander, disk sander, drum sander Spindle, orbital portable

## Slide 6: secondary processing
Sawing: Removing material using pointed cutting points equally spaced along the edge of a straight or round blade.
  Hand tools: Back saw, coping saw, keyhole, crosscut, rip
  Machine tools: Saber, jig or scroll saw, circular or table, radial arm, band saw

## Slide 7: Secondary Processing
Drilling: Removes material using a cutting tool with two or more spiral cutting edges.
  Hand Tools: Auger bit, twist drill, counter sink, forstner, brace,
  Machine Tools: Drill press, portable electric drill, Mill, Mortiser

## Slide 8: secondary processing
Turning: Cutting process in which a single cutting edge tool is fixed and work rotates.
  Hand Tools: Gouge, parting tool, Skew, facing tool
  Machine Tools: Lathe

## Slide 9: secondary processing
Shearing: Cutting using a single cutting edge moving through a fixed work piece.
  Hand Tools: plane, chisel, draw knife scraper
  Machine Tools: Jointer, veneer slicer

## Slide 10: Engineered wood panels
Examples include:
  Plywood
  MDF
  OSB
  Hardboard

## Slide 11: plywood
Constructed by gluing together layers (plies) of wood with the grain at right angels to each other.
Odd number of plies are used. (3,5,7)
Outer plies are called FACES (or face and back)
Next layers are called CROSSBANDS.
The other inside layer is called the CORE.
  2 most common types of cores are veneer and lumber.

## Slide 12: Types of plywood
2 types:
  Exterior:
  Interior:
    Difference between the 2 is the adhesive
      Plywood is available either softwood or hardwood.
4’x8’ standard size.
Thicknesses vary:
Grades: depends on the quality of the face and back veneers.

## Slide 13: Oriented strand board
OSB
Made of wood fibers adhered to each other with suitable resins and glues.
Arranged in layers at right angles to each other.

## Slide 14: Medium density fiberboard
MDF
Manufactured from a wood fiber-resin combination that is formed into a mat of random fiber orientation.
Hot press finished.
Smooth finish.
Excellent machinability

## Slide 15: Wood joinery – butt joints

## Slide 16: Wood joinery – miter joints

## Slide 17: Wood joinery – dado joints

## Slide 18: Wood joinery – Rabbet joints

## Slide 19: Wood joinery – box/finger joints

## Slide 20: Wood joinery – mortise and tenon

## Slide 21: Wood joinery – lap joints

## Slide 22: Wood joinery – butterfly joints

## Slide 23: Wood joinery – dowel

## Slide 24: Wood joinery – biscuit